ShenZhen JuRen Cheng Electronic Co.,LTD

Add：H6E031, 6 Floor, LED international trading center, FuTian district, ShenZhen, China

| 样 品 承 认 书 SPECIFICATION FOR APPROVAL |
| --- |
| 客 户 Customer: |
| 品 名 Product Name: 1WRGB 全彩大功率LED |
| 型 号Version number: 6C1WRGB 全彩 |
| 日 期 Deliver date: 2012-09-24 |
| 制造确认Product confirm and sign |
| 工程部 APPROVED BY | 制作 Manufacture | 审核 APPROVED BY |
| 客户确认Customer confirm and sign |
| 检查 TESTED BY | 审核 CHECKED BY | 承认 APPROVED BY |
| 确认后请回传,谢谢!Please confirm and fax to us ,thank you! Tel:0755-82787365 Fax:0755-82787360 |
| ● Package Dimensions 平面尺寸图Dimension（mm） Notes 1. All dimensions are in millimeters (inches). 2. Tolerance is ±0.25mm(0.010") unless otherwise noted. 3. Protruded resin under flange is 1.0mm(0.04") max. 4. Lead spacing is measured where the leads emerge from the package. 5. Specifications are subject to change without notice. ● Spatial Distribution |
| TEL:0755-82787365 Fax:0755-82787360 |
| ●Electrical / Optical Characteristics at TA=25℃ |
| Parameter | Symbol | Min. | Typ. | Max. | Unit | Test Condition |
| Luminous Intensity | ∮ | R | 25 | 30 | 35 | Lm | IF =350mA |
|  |  | G | 60 | 70 | 80 |  |  |
|  |  | B | 20 | 25 | 30 |  |  |
| Viewing Angle | 2θ1/2 | 95 | 100 | 105 | deg | IF =350mA |
| DominantWavelength | Λd | R | 620 | 625 | 630 | Nm | IF =350mA |
|  |  | G | 520 | 522 | 525 |  |  |
|  |  | B | 460 | 463 | 465 |  |  |
| Forward Voltage | vF | R | 2.2 | 2.3 | 2.4 | v | IF =350mA |
|  |  | G | 3.2 | 3.3 | 3.4 |  |  |
|  |  | B | 3.2 | 3.3 | 3.4 |  |  |
| Reverse Current | IR | 0 |  | 10 | uA | IF =350mA |

●Absolute  Maximum  Ratings  at  TA=25℃

| Parameter | Maximum Rating |
| --- | --- |
| Power Dissipation | 1W |
| Peak Forward Current(1/10 Duty Cycle, 0.1ms Pulse Width) | 400mA |
| Continuous Forward Current | 350mA |
| Derating Linear From 30℃ | 0.07mA/℃ |
| Reverse Voltage | 5V |
| Operating Temperature Range | -20℃ to + 80℃ |
| Storage Temperature Range | -30℃ to + 100℃ |
| Lead Soldering Temperature [1.6mm(.063") From Body] | 260℃ for 5 Seconds |
| TEL:0755-82787365 Fax:0755-82787360 |
| CAUTION THIS BAG CONTAINS MOISTURE AND ELECTROSTATIC SENSITIVE DEVICES |
| 使用注意事项 (1)存放 为了避免吸潮，建议这批产品储存在干盒(或放有干燥剂的盒子），或者以下环境推荐: 贮藏温度:5°C ~ 30°C湿度:60% HR MAX。 (2)产品打开之后的处理 SMD产品,当LED倾角焊、界面分离可能对光线传动效率,导致发光强度降低。以下的几项应当注意: A.打开产品后应尽快使用。 B.从打开一个未开封的包装贮藏温度测定值是:5°C ~ 40°C，湿度:30%HR MAX。 (3)处理未使用过的包装测定 如果储存超过1个星期或者如果标签、干燥剂材料有变化,部件应进行干燥处理为10 ~ 12小时，温度在在60°C %- p5°C%间。 (4)高湿度的储存 如果储存环境湿度高的产品高于使用干燥处理之前，推荐的干燥条件为:12小时，在100°C％P5°C间 (5)装置不应被使用于任何类型的流体,如水、油、有机溶剂等。在清洗时,应使用乙醇（酒精）。 (6)防静电措施，静电及喘振损害发光二极管。当把发光二极管拿在手中时,建议用防静电手套。所有设备、设备和机械应妥善接地。 |
| TEL:0755-82787365 Fax:0755-82787360 |